Limitations:
32b access (easy to enhance)
100MHz
Don't cares:
ODT constant
DQS-out (FPGA to SDRAM) single ended
DQS-in (SDRAM to FPGA) skipped

---
Testbench:	rtl\testbench\simple stimulus
Design:	rtl\system\fpga_top:	Executes test sequence on FPGA
Instantiates clock generator 100MHz => 100MHz
and SDRAM_CNTRL
rtl\system\SDRAM_CNTRL:
Generates proposed refresh mechanism
(Could hold initialization phase generator)
Instantiates PHYIO
rtl\system\SDRAM_PHYIO:
PHY: Instantiates DDR IOB registers
IO Handling FSM:
Initialization phase
SDRAM access control
Constraints:	constr\nexys4_ddr_sdram.xdc:
Constraints for SDRAM interface on NEXYS 4 DDR
constr\fpga_top.xdc: Project specific constraints.
Scripts:	script\report_io_timing.tcl: Script to generate IO timing report

---
Test sequence:	Initialization phase
Some basic writes and reads
Writes and reads to specific area (let's call it
area 3 because it is on bank 3)
Loop over writes and reads throughout some banks.
If everything works fine, led(1) turn on.
In general, if a bug was found, led(1) turns off and
led(0) blinks fast (every second).
After ca. 1 minute, area 3 is read again to check, if
the refresh mechanism worked. If yes, led(0) toggles
to indicate this 1 minute interval and that the testcase
is still active.

---
FPGA
DDR2 SDRAM
4,652ns
        DQ
3,106ns
      3,142ns
        DQS
5,772ns
        CTRL

---
FPGA
4,652ns
        DQ
3,106ns
      3,142ns
        DQS
5,772ns
        CTRL

---
FPGA
DDR2 SDRAM
???
9ns … 10ns … 11ns
4,652ns

---
Optimizations:
64b, 128b
Bytewise write
Faster clock
Faster access, multiple active banks
…
More standalone testing
=> PDVL